## Slide 1: IoT with the ESP8266
and NodeMCU Firmware
Jason Follas Sr. Software Engineer Quicken Loans
@jfollas

## Slide 2: Agenda
Espressif makes a highly integrated SoC known as the ESP8266-EX that combines a microcontroller with a Wi-Fi stack on the same silicon. This chip, combined with flash memory and an antenna, is sold as a FCC/CE-approved module for under US$3. Breadboard-friendly DevKits that combine the module with USB serial port and power components are available for under US$7.
This talk is not a sales pitch for Espressif, though. Rather, we will explore how to write software for this tiny platform, primarily focusing on the use of an open-source firmware known as NodeMCU. Using scripts written in Lua, we’ll see how to connect to a network, read data from other devices and sensors, and communicate with services on the internet – the types of activities that a tiny Thing would need to do!

## Slide 3: In my experience, the Internet of Things is kind of expensive…

## Slide 5
Energy Metering
Send to Cloud
5-Second Sleep

## Slide 6: We needed a platform.

## Slide 7: Raspberry Pi 3
$40

## Slide 8: Arduino UNO R3
$25

## Slide 9: Arduino Pro Mini 328
$10
5VDC
Atmel ATmega328 16MHz
8 Analog Pins 14 Digital Pins
32KB Flash
1KB EEPROM
2KB SRAM

## Slide 10: Raspberry Pi Zero
$5

## Slide 11: But what about the “I” in IoT?

## Slide 12: Arduino Yun
$80
ATmega32u4 +
Atheros AR9331

## Slide 13: Arduino Yun Mini
$65
ATmega32u4 +
Atheros AR9331

## Slide 14: Particle Photon
$20
Broadcom BCM43362 Wi-Fi Chip
STM32 120MHz Cortex M3 128KB RAM 1MB Flash
Particle Cloud

## Slide 15: Raspberry Pi Zero W
$10

## Slide 16: ESP8266-01 Serial-to-Wi-Fi
$2
AT commands
802.11 b/g/n

## Slide 17
RST
Vcc
GND
GPIO2
GPIO0
Rx
Tx
CH_ PD

## Slide 18: Introducing the ESP8266

## Slide 19: ESP8266EX
Microcontroller
RAM
Wi-Fi
GPIO

## Slide 20: AI Thinker Modules

## Slide 21: AI Thinker Modules

## Slide 22: Breadboard-friendly Dev Kits
Adafruit ESP8266 Huzzah
$10

## Slide 23: Breadboard-friendly Dev Kits
Adafruit Feather Huzzah
$16

## Slide 24: Breadboard-friendly Dev Kits
Wemos D2
$4

## Slide 25: Breadboard-friendly Dev Kits
NodeMCU DevKit
$5

## Slide 26: ESP8266 By The Numbers

## Slide 27: ESP8266 By The Numbers
32-bit RISC processor based on the Tensilica Xtensa Core
32

## Slide 28: ESP8266 By The Numbers
80MHz or 160MHz (selectable in software)
80/160

## Slide 29: ESP8266 By The Numbers
Price of the ESP8266EX chip itself
<1

## Slide 30: ESP8266 By The Numbers
Price of the ESP8266-12F module by AI Thinker
2

## Slide 31: ESP8266 By The Numbers
3.3 Volts
3.3

## Slide 32: ESP8266 By The Numbers
80 KB Data RAM 35 KB Instruction RAM (Harvard architecture)
80/35

## Slide 33: ESP8266 By The Numbers
GPIO Pins
16

## Slide 34: ESP8266 By The Numbers
Analog-Digital Converter 0-1 VDC range
1

## Slide 35: ESP8266 By The Numbers
802.11 b/g/n Wi-Fi built into the silicon
802.11

## Slide 36: ESP8266 By The Numbers
2.4 GHz radio band only
2.4

## Slide 37: ESP8266 By The Numbers
Chips sold
30,000,000+

## Slide 38: Wi-Fi
802.11 b/g/n, 2.4 GHz band only
Modes:
  Station
  SoftAP
  Station + SoftAP
Warning: Only one radio channel! Station+SoftAP must share

## Slide 39: Power Requirements
40 uA idle
400 mA spikes (i.e., during Wi-Fi broadcasting)
 | Standby | Always On | Wake every 1 minute | Wake every 1 hour
2xAA alkaline 3000mAh | 8.4 years | 44 hours | 18.6 days | 827 days
Credit: Baoshi Zhu http://www.slideshare.net/baoshi1/build-wifi-gadgets-using-esp8266

## Slide 40: Firmware

## Slide 41: AT Firmware
Default firmware on AI Thinker modules
Serial-to-WiFi functionality
AT+CWJAP="YOURSSID","password"

## Slide 42: ESP8266 SDK
C libraries to create your own firmware (API to the hardware)
Two versions:
Non-OS SDK (timers and callbacks)
RTOS SDK (based on FreeRTOS)

## Slide 43: Open Source Firmware Projects/Frameworks
MicroPython https://github.com/micropython/micropython/
ESP8266Basic http://www.esp8266basic.com/
Espruino (JavaScript) http://www.espruino.com/ESP8266
Sming (C++) https://github.com/SmingHub/Sming
Arduino support for the ESP8266 https://github.com/esp8266/arduino

## Slide 44: Arduino Uno Compatible!
Wemos D1 R2
$7

## Slide 45: NodeMCU Firmware
https://github.com/nodemcu/nodemcu-firmware
Companion project for the open source NodeMCU Dev Kit hardware (but will work on any ESP8266)
SDK is abstracted through a Lua language service/REPL
Firmware is the “Operating System”
Scripts are the “Application”
40+ modules to interface with internal and external hardware

## Slide 46
ESP8266 Microcontroller + Wi-Fi
ESP8266 SDK
Flash Memory
AI Thinker ESP-12F Module
SJSON
SPI
FILE
WIFI
RTC
NET
HTTP
MQTT
GPIO
NODE
ADC
CRYPTO
eLua (NodeMCU Firmware)
Lua Scripts

## Slide 47: Build the Firmware
http://nodemcu-build.com/

## Slide 48: Build the Firmware Yourself
Need Linux* (a virtual machine or WSL will work on Win10)
Need Xtensa Toolchain (for cross compiling)
Need NodeMCU Firmware Source Code
*Linux not absolutely required, but is the first-class environment that will be the easiest to get going

## Slide 49: Build the Firmware Yourself: Toolchain

## Slide 50: Flashing the Firmware

## Slide 51: Flashing Firmware: RESET Requirements
GPIO15: Low
GPIO2: High
GPIO0: Low to Flash High to Run

## Slide 52: Flashing Firmware: NodeMCU Firmware Programmer

## Slide 53: Flashing Firmware: esptool (primarily Linux)
> esptool.py --port /dev/ttyUSB0 write_flash 0x00000 firmware.bin
Connecting...
Erasing flash...
Writing at 0x00000000... (0 %)
https://github.com/themadinventor/esptool
(NOTE: Windows Subsystem for Linux (WSL) does not support COM ports)

## Slide 54: A Brief Primer on Lua

## Slide 55: Comments
-- This is a comment
--[[
This is a block comment
--]]

## Slide 56: Types
nil
boolean
number
string
function
table

## Slide 57: Boolean
true or false
In conditionals, false and nil are considered false. Everything else is true
Warning: This means "" and 0 are both considered true

## Slide 58: Number
All numbers are double-precision floating points
Still treat integers like integers – the language will sort it out

## Slide 59: String
Either single quote ( ' ) or double quotes ( " ) for literals
Concatenation operator is double-dot ( .. )
Lua automatically converts between types:
  print("10" + 1)  11
  print("hello" + 1)  ERROR
  print("hello" .. 1)  "hello1"

## Slide 60: Tables
Associative arrays (key/value pairs)
Used to represent ordinary arrays, sets, records, queues, classes, and other data structures
a = {}
a[1] = "hello"
a["x"] = "world"
print(a.x)  "world"

## Slide 61: Relational Operators
<
>
<=
>=
==
~=

## Slide 62: Logical Operators
and
or
not
x = x or v  if not x then x = v
a and b or c  a ? b : c

## Slide 63: Assignment
> a = "hello" .. "world
> t.n = t.n + 1
> a, b = "hello", "world"
> x, y = y, x

## Slide 64: Global Variables
> print(b)
nil
> b = 10
> print(b)
10
> b = nil
> print(b)
nil

## Slide 65: Local Variables
> b = 10
> do
>> local b = 12
>> print(b)
>> end
12
> print(b)
10

## Slide 66: Control Statements: if then else
> if b == 12 then print("yes") end
> if b == 12 then
>> print("yes")
>> elseif b < 10 then
>> print("no")
>> else
>> print("don't know")
>> end

## Slide 67: Control Statements: while
> while true do
>> print("The Neverending Story!")
>> end

## Slide 68: Control Statements: for
> for i=1,10 do
>> print(i)
>> end
> for i=10,1,-1 do
>> print(i)
>> if i == 5 then break end
>> end

## Slide 69: Control Statements: for (with iterator)
> for k,v in pairs(_G) do
>> print(k)
>> end

## Slide 70: Functions
> function add(a,b)
>> return a+b
>> end
> print(add(1,2))
3

## Slide 71: Functions: Multiple return values
> function foo()
>> return 1, 2, 3, 4
>> end
> a, b, c, d = foo()
> a, b = foo()
> a, _, _, d = foo()
> a, b, c, d, e, f = foo()

## Slide 72: Functions: Calling an instance function
> function MyClass.foo(self)
>> return 123
>> end
> a = MyClass.foo(some_instance)
> a = some_instance:foo()

## Slide 73: Write an App

## Slide 74: Write an App
Connect to Wi-Fi
Read value from sensor
Publish to MQTT
Repeat

## Slide 75: Adafruit BMP280

## Slide 76: SparkFun BME280

## Slide 77: DEMO: Write an App

## Slide 78: Gotchas

## Slide 79: Memory Issues
At reset without doing anything, we have about 40 KB of RAM available to be used.
When you run out of memory, you die. Known as a Panic-Reset.
This heap is managed by Lua when C allocation is performed by Lua’s alloc
  NodeMCU modules can leak if malloc/free is not properly performed
Lua has a garbage collector, but will not free memory that is referenced by something else
  This can really hurt when you have chunks that call chunks that call chunks, etc.

## Slide 80: Memory Optimization
Use smaller *.lua file sizes
Entire script must be loaded into memory
  The longer the script, the less memory is available for data (and other scripts)
Through trial and error, found that < 5 KB was a good target

## Slide 81: Memory Optimization
Compile *.lua scripts into bytecode (*.lc files) when possible
All code is compiled into bytecode anyways
node.compile("script.lua")
This removes debugging information
This also prevents the double-memory penalty:
  Once for loading the entire script string into memory
  Once again for compiling into bytecode (then the string can be freed)
  If there’s not enough heap space for both, then it will Panic

## Slide 82: Memory Optimization
FlashMod
Technique based on the fact that Lua can provide dynamic function invocation
Functions within a Flash Module are serialized to bytecode and saved in Flash
When invoked, the bytecode is (dynamically) loaded from Flash Memory and then executed
Breaks up a big chunk into lots of little easily-disposed chunks

## Slide 83: Memory Optimization
Think of code as tasks
If a chunk of code invokes another chunk, then memory for the first chunk will not be freed until the second is done running
Chunk can instead schedule another chunk to run as a task.
  Original Chunk is freed and garbage collected at the end of execution
  Lua will run the highest priority task from the task queue next.
  This has the same effect as calling a function, with different semantics

## Slide 84: Exciting things are in the works!

## Slide 85: The future is Now! ESP32
New chip based on two cores
  One core for your app
  One core dedicated to its hardware
More RAM
More GPIO
Faster Wi-Fi
Bluetooth (BLE)
All on a single chip
For a little more money

## Slide 86: Thanks for Listening!

## Slide 87: Resources
NodeMCU Firmware https://github.com/nodemcu/nodemcu-firmware
NodeMCU Build http://nodemcu-build.com/
A good $7 NodeMCU DevKit sold by Banggood http://bit.ly/28Uwc4x

## Slide 88: Resources
ESP8266.com http://esp8266.com/
AdaFruit https://www.adafruit.com/
Lua 5.1 Reference https://www.lua.org/manual/5.1/

## Slide 89: Contact Information
Jason Follas
Quicken Loans
jasonfollas@quickenloans.com
Twitter: @jfollas
This presentation and code can be found here: https://github.com/jfollas/mqttdemo
#10
#1